## Slide 1: Acoustics Sound Measurements
Dr. Hassan Hassoon ALDelfi
ARCH 426

## Slide 2: Objectives
1- To Highlight Acoustics’ fundamentals and terminologies.
2- To discuss aspects for applications in built environment.
3- Acoustical Design and Treatment

## Slide 3: Sound pressure
Sound Pressure : is any deviation( dynamic pressure) in the static pressure of the ambient transmission medium as shown:
Sound pressure diagram: 1. silence; 2. audible sound; 3. atmospheric pressure; 4. sound pressure-dynamic pressure

## Slide 4: A, B and C Standard filters Countours
Standard filter contours are used to
make the instrument more nearly
approximate the normal human ear.
The different contours were intended
to match the ear at different sound
intensities

## Slide 5: Sound Pressure Level Measuring scales
 | Octave Band Center Frequency (Hz) |  |  |  |  |  |  |  | 
 | 31.25 | 62.5 | 125 | 250 | 500 | 1000 | 2000 | 4000 | 8000
Measured or Estimated Sound Pressure Level dB | 30 | 54 | 60 | 64 | 53 | 48 | 43 | 39 | 32
Resulting with dB(A) filter | 0 | 27.8 | 43.9 | 55.4 | 49.8 | 48 | 44.2 | 40 | 30.9
Resulting with dB(B) filter | 13 | 45 | 56 | 63 | 53 | 48 | 43 | 38 | 29
Resulting with dB(C) filter | 27 | 53.2 | 59.8 | 64 | 53 | 48 | 42.8 | 38.2 | 29
dB(A) filter | -39.4 | -26.2 | -16.1 | -8.6 | -3.2 | 0 | 1.2 | 1 | -1.1
dB(B) filter | -17 | -9 | -4 | -1 | 0 | 0 | 0 | -1 | -3
dB(C) filter | -3 | -0.8 | -0.2 | 0 | 0 | 0 | -0.2 | -0.8 | -3

## Slide 6: Sound Pressure Level
The human ear can hear a broad range of sound pressures. Because of this, the
sound pressure level (SPL) is measured in decibels (dB) on a logarithmic scale that compresses the values into a manageable range. In contrast, direct pressure is measured in Pascals (N/ N/m2) SPL is calculated as 10 times the logarithm of the square of the ratio of the instantaneous pressure fluctuations (above and below atmospheric pressure) to the reference pressure:
SPL = 10 × log10(P/Pref)2
P is the instantaneous sound pressure, in units Pa or N/m2 and Pref = 20x10-6is the reference pressure
Reference pressure defined as the quietest noise a healthy young person can hear (20 µPa).

## Slide 7: Example
If a piece of equipment has a sound pressure of 2 Pa, what will be the resulting sound pressure level ?
SPL = 10 × log10(P/Pref)2
SPL = 20 × log10(P/Pref)
Substitute in above
SPL = 20 log10 (2/0.00002)
= 20 log10(100,000)
= 20 × 5.0 = 100 dB

## Slide 8: Sound Power Level
Sound Power Level (Lw) is similar in concept to the wattage of a light bulb.
In fact, Lw or (SWL)is measured in watts (W). Unlike Lp (SPL). Lw does not depend on the distance from the noise source.
The sound power level is calculated using the following equation:
SWL=Lw = 10 × log10(W/Wref)
Where W is the acoustic power in watts and Wref is the reference acoustic
power, 10‐12
.

## Slide 9: Example
The sound power level associated with a typical face‐to‐face conversation, which may have a sound power of 0.00001 W,
is calculated:
SWL= Lw = 10 × log10(0.00001/10‐12) = 70 dB

## Slide 10: Sound Wave
In a sound wave, the complementary variable to sound pressure is the particle velocity. Together they determine the sound intensity of the wave.
Sound intensity, denoted I and measured in W/m2 in SI units, is defined by
I = pv………. W/m2
p is the sound pressure; N/m2
v is the particle velocity. m/S

## Slide 11: Noise: is defined as the unwanted sound which causes unpleasant and discomfort to ears.
Noise can come from many places, types of noise sources are:
1-Gadgets like food mixer, grinder, vacuum cleaner, washing machine and dryer, cooler, air conditioners, can be very noisy and injurious to health. Others include loud speakers of sound systems and TVs, ipads and ear phones. Another example may be your neighbor’s dog barking all night everyday at every shadow it sees, disturbing everyone else in the apartment.
2-Social events: Places of discos, parties and other social events also create a lot of noise for the people living in that area. In many market areas, people sell with loud speakers, others shout out offers and try to get customers to buy their goods. It is important to note that whey these events are not often, they can be called 'Nuisance' rather than noise pollution. ( ISAAJ)

## Slide 12
3-Commercial and industrial activities: Printing presses, manufacturing industries, construction sites, contribute to noise pollutions in large cities. In many industries, it is a requirement that people always wear earplugs to minimize their exposure to heavy noise. People who work with lawn mowers, tractors and noisy equipment are also required to wear noise-proof gadgets.
4-Transportation: Think of aero planes flying over houses close to busy airports like Dubai Baghdad, and Erbil Airports, over ground and underground trains, vehicles on road—these are constantly making a lot of noise and people always struggle to cope with them.

## Slide 13: Nuisance :A few good examples of nuisance include:
Barking dogs
Building and construction site noise (please note however that noisy Work is permitted between 8am and 6pm Sunday to Thursday, and 8am to 1pm on Saturdays)
DIY noise during anti-social hours
Burglar / car alarms
Noisy deliveries at unreasonable hours
Parties, Nightclubs and pubs
Loud music / television / computer games
Industrial processes (dry cleaners, factories etc)
Kitchen extract / air conditioning units
Open-air event and street performers

## Slide 14: Room Acoustics:
There are many factors that influence the sound in a given space:
Room Size: the longer dimension should contain the low frequency wave for good listening, larger size larger loudspeaker and low size smaller size loudspeaker. f = c / λ = wave speed c (m/s) / wavelength λ (m). The formula for time is: T (period) = 1 / f (frequency). λ = c / f = wave speed c (m/s) / frequency f (Hz). The unit hertz (Hz) was once called cps = cycles per second. the speed of sound is 343.2 metres or 1,236 km/h

## Slide 15: Materials
Rigidity And Mass: the more rigid/massive the walls, floor and ceilings in our listening rooms, the less diaphragmatic action and the tighter, more defined and powerful the bass. *(flexture ) Our goal then, is to reduce the amount of diaphragmatic action in the listening room. We can accomplish this task by increasing the mass and rigidity of all surfaces within the listening environment
Reflectivity Live and Dead Rooms:In simple terms, reflectivity is the apparent "liveness" of a room. Professionals prefer the term reverb time( reverberation time) or Rt-60. Rt-60 defined, is the amount of time (in seconds) it takes for a pulsed tone to decay to a level 6OdB below the original intensity. A live room has a great deal of reflectivity, and hence a long Rt-60. A dead room has little reflectivity and a short Rt-60.

## Slide 16: Combining and Averaging Sound Levels
Decibels are measured using a logarithmic scale, which means decibels cannot be added arithmetically. For example, if two noise sources are
each producing 90 dB right next to each other, the combined noise level will be 93 dB, as opposed to 180 dB. The following equation should be used to calculate the sum of sound pressure levels, sound intensity
levels, or sound power levels:
Total L = Total SPL =
=10x9.3=93 dB
Often, using this equation to quickly sum sound levels when there is no
calculator or computer available is difficult. The following table can be used to estimate a sum of various
sound levels.

## Slide 17: Combining Sound Levels
Difference Between Two Levels to Be Added
Amount to Add to Higher Level to Find the Sum 0–1 dB 3 dB 2–4 dB 2 dB 5–9 dB 1 dB 10 dB 0 dB
Example: There are three noise sources immediately adjacent to one another, each producing a
sound level of 95 dB. The combined sound level can be found using the table above.
Ans: The difference between the first two noise sources is 0 dB, which means the sum will be 95 + 3 = 98 dB.
The difference between (98 dB ) and the remaining noise source (95 dB) is 3, which means the sum will be 98 + 2 = 100 dB.
Difference in Levels dB | dB to be added to the higher level
0 to 1 | 3
2 to 4 | 2
5 to 9 | 1
10 to higher | 0

## Slide 18: Occupational Safety and Health Administration (OSHA)
Adding Noise Exposure Durations to Determine Compliance with
OSHA Standards
The Act created the Occupational Safety and Health Administration (OSHA), which sets and enforces protective workplace safety and health standards. OSHA also provides information, training and assistance to workers and employers.
Under OSHA standards, workers are not permitted to be exposed to an 8‐hour TWA equal to or greater than 90 dBA ( Time Weighted Average). OSHA uses a 5‐dBA exchange rate, meaning the noise level doubles with each additional 5 dBA. The following chart shows how
long workers are permitted to be exposed to specific noise levels:

## Slide 19
Permissible Duration (Hours per Day)
Sound Level (dBA, Slow Response) 16 85 8 90 4 95 2 100 1½ 102 1 105 ½ 110 ¼ or less 115
Permissible Duration ( Hours per Day) | Sound Level dBA
16 | 85
8 | 90
4 | 95
2 (1/4) | 100 (115)

## Slide 20: Combining Low and High Sound Levels
A worker’s daily noise exposure typically comes from multiple sources, which have different noise levels for different durations.
When adding different noise levels from various noise sources, only
noise levels exceeding 80 dBA should be considered. The combined effect of these noise sources can be estimated using the following equation:
Sum SPL = C1/T1 + C2/T2 + C3/T3 + ……………….+Cn/Tn
Where Cn is the total duration of exposure at a specific noise level, and
Tn is the total duration of noise permitted at that decibel level.
If the Sum SPL the combined noise level is greater than the allowable level.
If the Sum SPL the combined noise level is less than the allowable level.

## Slide 21: Sound Propagation & Room Attenuation for Sound Levels:
• Reverberation Time - Sound Reverberation Time indicates the time it takes until the sound pressure level in a room is decreased with 60 dB
• Directivity Coefficient and Sound Attenuation - The attenuation in a room depends on the location of the source and the receiver, and the room constant
• Room Absorption Characteristics - Mean absorption coefficients and reverberation times for some typical rooms
• Room Attenuation in Direct Sound Fields - Room size - absorption characteristics and attenuation in direct sound fields
• Sound Intensity - Sound intensity level is the acoustic power of sound per unit of area in relation to a fixed reference
• Sound Absorption Coefficients for some common Materials - Sound absorption coefficients for some common materials as plaster walls, brickwork, plywood panels etc...
• Sound Pressure - Sound Pressure is the force of sound on a surface area perpendicular to the direction of sound

## Slide 22: Sound Absorption Materials
The sound absorption coefficient is the ratio of absorbed sound intensity in an actual material to the incident sound intensity and can be expressed as
α = Ia / Ii
Room attenuation ( Lp-LN) depends on location of source and receiver - and the room constant R
For a continuing sound source the sound level in a room is the sum of Direct and
Reverberant Sound. The sound pressure for a receiver can be expressed as
Lp = LN + 10log (D / (4 π r2) + 4 / R) (1)
where
Lp = received sound pressure level (dB) or SPL
LN = sound power level from source (dB) or SWL
D = directivity coefficient as shown in figure below
R = room constant (m2 Sabine), OR R = Σ Si αi / (1- αm) or R = A / (1- αm) ….(2)
π = 3.14 ....., A= sound absorption in m2sabine, Si αi individual service area and absorption coefficient respectively.
r = distance from source (m)

## Slide 23: Directivity coefficient - D
The figure below can be used to approximate the Directivity coefficient - D - for typical locations of the receiver and the sound source. The figure below can be used to approximate the Directivity coefficient - D - for typical locations of the receiver and the sound source
D - directivity coefficient

## Slide 24: Attenuation Between Source and Receiver
Noise and Attenuation - Noise is usually defined as unwanted sound - noise, noise generation, silencers and attenuation in HVAC systems.
The given equation of Lp can be transformed to express the difference between the received sound pressure level and emitted sound power level - the attenuation - as:
Lp - LN = 10 log (D / (4 π r2) + 4 / R) (2)
The room constant express the acoustic property of a room.
R = A / (1- αm)
OR R = Σ Si αi / (1- αm) (3) and αm= A/S
αi…… depends on frequency

## Slide 25
The sound absorption coefficient indicates how much of the sound is absorbed in the actual material. The absorption coefficient can be expressed as:
α = Ia / Ii (1)
where Ia = sound intensity absorbed (W/m2)
Ii = incident sound intensity (W/m2)
Concrete block, coarse | 0.3 - 0.4
Concrete block, painted | 0.05 - 0.07
Cork sheet, 6 mm | 0.1 - 0.2
Fiberboard on battens, 12 mm | 0.3 - 0.4
Floor, concrete or terrazzo | 0.02
Floor, linoleum, asphalt, rubber or cork tiles on concrete | 0.03
Floor, wood | 0.06 - 0.1
Hardwood | 0.3
Glass, large panes heavy plate | 0.03 - 0.05
Glass, ordinary windows | 0.1 - 0.2
Gypsum board, 12 mm | 0.04 - 0.07
Mineral wool, 100 mm | 0.65
Persons, each | 2.0 - 5.0
Plaster walls | 0.01 - 0.03
Plywood panel, 3 mm | 0.01 - 0.02
Polystyrene, expanded on 50mm battens | 0.35
Polystyrene, expanded rigid backing | 0.15
Polyurethane foam, flexible | 0.95
Rubber sheet, 6 mm porous | 0.1 - 0.2
Slag wool or glass silk, 50 mm | 0.8 - 0.9
Snow | 0.75
Wood wool cement on battens, 25 mm | 0.6 - 0.07

## Slide 27: Room Acoustical Properties
Room acoustics and acoustic properties - decibel A, B and C weighing curves or Scales- Noise Rating (NR) curves, Loudness in PHON, Noise Criteria Curve (NC), sound transmission, sound pressure, sound intensity and sound attenuation.

## Slide 28: Some Typical Sound Levels
Sources at 1 m | Sound Pressure | Lp re 20 µPa * (SPL)
Rifle | 200 Pa | 140 dB
Threshold of pain | 20 Pa | 120 dB
Pneumatic hammer | 2 Pa | 100 dB
6 dB = double the Pa | 1 Pa | 94 dB
Street traffic | 0.2 Pa | 80 dB
Talking | 0.02 Pa | 60 dB
Library | 0.002 Pa | 40 dB
TV Studio | 0.0002 Pa | 20 dB
Threshold of hearing | 0.00002 Pa | 0 dB

## Slide 30: THE EQUAL LOUDNESS COUNTOURS

## Slide 31: A, B and C Standard filters Countours
Standard filter contours are used to
make the instrument more nearly
approximate the normal human ear.
The different contours were intended
to match the ear at different sound
intensities

## Slide 32: Sound Pressure Level Measuring scales
 | Octave Band Center Frequency (Hz) |  |  |  |  |  |  |  | 
 | 31.25 | 62.5 | 125 | 250 | 500 | 1000 | 2000 | 4000 | 8000
Measured or Estimated Sound Pressure Level dB | 30 | 54 | 60 | 64 | 53 | 48 | 43 | 39 | 32
Resulting with dB(A) filter | 0 | 27.8 | 43.9 | 55.4 | 49.8 | 48 | 44.2 | 40 | 30.9
Resulting with dB(B) filter | 13 | 45 | 56 | 63 | 53 | 48 | 43 | 38 | 29
Resulting with dB(C) filter | 27 | 53.2 | 59.8 | 64 | 53 | 48 | 42.8 | 38.2 | 29
dB(A) filter | -39.4 | -26.2 | -16.1 | -8.6 | -3.2 | 0 | 1.2 | 1 | -1.1
dB(B) filter | -17 | -9 | -4 | -1 | 0 | 0 | 0 | -1 | -3
dB(C) filter | -3 | -0.8 | -0.2 | 0 | 0 | 0 | -0.2 | -0.8 | -3

## Slide 34: AIR-HANDLING UNIT

## Slide 36: AHU SCHEMATIC

## Slide 37: Example - Acoustic Calculation of a Ventilation System

## Slide 38: Noise pollution prevention and control tips
noise and nuisance Construction of soundproof rooms for noisy machines in industrial and manufacturing installations must be encouraged. This is also important for residential building—noisy machines should be installed far from sleeping and living rooms, like in a basement or garage.
noise and nuisance Use of horns with jarring sounds, motorbikes with damaged exhaust pipes, noisy trucks to be banned.
noise and nuisance Noise producing industries, airports, bus and transport terminals and railway stations to sighted far from where living places.

## Slide 39: Wall and ceiling acoustic treatment
The most common are the 500 series of compressed Fiberglas panels. These can be covered with an open-weave cloth and used either as spot treatment for reflection control or general room deadening.

## Slide 40
THANKS